## Slide 1: What is I²C
A bus for Inter-Integrated-Circuit communication
▶ Design for hardware simplicity: 2 wires, many chips per bus, flexible
▶ Not discoverable, not plug-and-play
▶ Low speed: 100-400 kHz (with 1 MHz and 3.4 MHz extensions)
▶ Also known as: I2C, IIC, TWI, TWSI, …

## Slide 2: Roles
Adapter
▶ Other names: Master, Controller, bus
▶ Initiates all transactions
▶ Usually one (multimaster possible)
▶ Has no address
Client
▶ Other names: Slave, Device
▶ Responds to transactions
▶ Many per bus
▶ 7-bit address set in hardware
(10-bit extension)

## Slide 3: Two wires
▶ Two wires
• SDA: data, bidirectional
• SCL: “clock”
Not really a clock
SDA moved at SCL falling edge, SDA read at SCL rising edge
Mostly driven by adapter, sometimes also by clients (clock stretching)
▶ Open collector

## Slide 4: Communication protocol
1. Start condition
2. Adapter sends: client address (7 bit) + direction bit (R/W)
3. Client sends ACK
4. Client sends one byte
5. Adapter sends ACK
6. Stop condition